TOPICS LEARNED :
Revising of multipliers like wallace multipliers

AIM :
To design the basic block of wallace multiplier.

APPARATUS (Tools used) :
Xilinx for writing basic codes , cadence (genus for producing rtl schematic , innovus for	looking into floor plan and optimizing the design in terms of power and area , fpga boards	and digilent to dump the bit file generated by xilinx to see the output )

PROCEDURE :

1... XILINX :
1. We have written the codes all the adders and generated the test bench using the	text fixture in Xilinx

2. Then we have created ucf file containing constraints of the verilog code for	wallace multiplier.

3. Then we have taken screen shots of timing diagrams and produced the	rtl_schematic to see the loguc diagram and taken screen shot then finally produced a	programmable bit file to dump into the fpga board which we can use by the pins	declared in ucf file.

4. then we have produced the test poer and documented the area,power,timing delay	in design summary .

2... CADENCE :

1. NCLAUNCH :
1. Here we know that in Xilinx we have used a single project to code every	adder so we need not add the modules of smaller adders .But in cadence it is	not in such way so we need to add the modules of smaller ones so that they	can be called as functions.

2. So after copying those codes including modules and test fixtures we	uploaded them to nclaunch tool and saw the output of timing diagram and	have observed that it gives the output in hexa decimal format .

3. Then we have taken screen shots of timing diagrams of those adders
2. GENUS :
1. Then we have used the tool genus to produce the rtl schemaic diagram and	taken the outputs of cell count ,area,power,netlist,timing with help of	rc_script.tcl code and	copied	them into table to compare outputs of innovus	and genus.

3.INNOVUS :
1.In this we have used the file Default.globals to start with and then built the	circuit	digitally with requirements and learnt to use floor plan,we have used 9	floors and metal 9 which is lowest resistivity .

2.Then we have optimised the design using	nano route, calculated the timing	using	pre_place,pre_cts,post_cts,post_route,signoff,eco to finally optimise	the design .then we have reported area,power using terminal and copied	them ,then finally we saved the project and then reported netlist statistics and	then saved netlist file generated by innovus,then we have screen shots of the	design in innovus.
COMMANDS USED :
1.ssh -X root@10.2.20.7
2.csh
3.source cshrc
4.nclaunch
5.genus -f rc_script.tcl -gui
6.innovus
7.report_area
8.report_power
9.scp -r root@10.2.20.7:ASIC_DESIGN/VLSI_DESIGN_2019/Mohit_2018102016/assign2	./Desktop/sem\ 2\ 1/vlsi/assign2/

LINKS USED :(reference)
https://drive.google.com/open?id=1DkpjyA1jlUY42pv-zL3H0AUn_PxH4NKe
Www.asic_world.com
https://moodle.iiit.ac.in/mod/resource/view.php?id=20109
https://moodle.iiit.ac.in/mod/resource/view.php?id=20110
https://moodle.iiit.ac.in/mod/page/view.php?id=20108

PRECAUTIONS (While doing assign):

 In Xilinx : If the inputs are much more than input pins in fpga board and if we tried to	create the constraints file then it will show the segmentation fault and exits from the xilinx.

In Innovus : The optimisation further can`t be done after doing signoff.

LEARNT TOPICS :

1.Using arrays
2.Observing the timings diagrams of arrays
3.Using digilent anf fpga boards.
4.xilinx area,timing,power reporting
5.floor plan.
6.sign_off timing.
7.writing bit code and ucf files

OBSERVATION:
We have observed that the innovus is optimizing the block and genus is producing the rtl	schematic and nc launch is producing timing graph .

DIGITAL BLOCK	AREA / GENUS (um^2) INNOVUS(um^2)		POWER / GENUS (nW) INNOVUS(mW)
Wallace_tree multiplier	303.517	303.5169	10722.413	0.008248

CONCLUSION :
We have used half adders and full adders to complte the addition so that at each level 3 bits	can be added at once unlike the normal multiplier so that the number of levels are	minimised. Hence the timing and power too.
We have learnt how to use wallace _tree multiplier and we have known the advantages	and	disadvantages of both the adders .
Ripple adder is more advantageous compared to (delay*power the coomon factor)	look_ahead adder.
Innovus optimises the circuit with respect to area,power,time delay and it decreases	resistance with its floor plan.